## Motor Grader 724M

Configuration of Motor Grader 724M
Length×width×height(mm): 9230×2800×3550
Max. traction force(KN): 99
Min. turning radius(mm): 8600

1. Engine
Type: water-cooled, four-stroke, turbocharged engine
Model: Caterpillar SC11CB from Shanghai Diesel Engine Co., Ltd. (with Caterpillar license 3306B) 
Rated power: 175kW/240ps
Rated speed: 2600rpm/2300rpm
Max. torque: 750Nm at 1500-1700rpm, 843Nm at 1400rpm

2. Gearbox of Motor Grader
Model: ZF from Liuzhou 
Type: power shift, electric hydraulic control, with torque converter
Gear shift position: 6 forward and 3 reverse gears
Travelling Speed

Specifications of Motor Grader

| Speed/Gear | 1 | 2 | 3 | 4 | 5 | 6 |
| --- | --- | --- | --- | --- | --- | --- |
| Forward(km/h) | 5.74 | 8.73 | 13.02 | 17.49 | 26.98 | 38.98 |
| Reverse(km/h) | 5.74 | 13.02 | 26.98 | - | - | - |

3. Axle of Motor Grader
3.1 Rear axle: 3-stage drive axle with NO-SPIN differential mechanism
3.2 Front axle: oscillating driven axle, with the oscillating angle of 15° (left and right), 17° tilting angle of front wheel (left and right), and 45° steering angle

4. Tandem Box
Type: oscillating type
Oscillating angle: 15°
Drive: heavy-duty roller chain

5. Braking System
5.1 Service brake: fully hydraulic driven, the caliper disc brakes for the road grader are located beside the two middle wheels and the two rear wheels.
5.2 Stopping brake: the hub brake is installed on the shaft end of the gearbox.
5.3 Continuous braking: the torque converter supports continuous braking.

6. Hydraulic System of Motor Grader
Installed with independent double pump double-circuit system, the hydraulic system for the construction machinery provides the system pressure of 16MPa.

7. Frame 
Articulated frame

8. Blade of Motor Grader
Size: 4422×688 (length×chord height)
Rollback angle: 360°
Max. slant angle (L/R): 90°
Max. grading depth: 500mm

9. Tire
Type: standard tire installed on the road construction machinery
Quantity: 6
Size: 20.5-25, 16PR

10. Electrical System and Instrument
Working voltage: 24V
Instrument: various work lights and instruments engineered for the land leveller

11. Main Technical Specifications
11.1 Operating weight: 19000kg (standard)/20000kg (with front dozer and rear ripper) 
11.2 Overall dimensions: 9300×2800×3800 (standard), 10910×2890×3630 (with front dozer and rear ripper)

12. Optional Parts of Motor Grader
12.1 Front dozer for the land grading machine
12.1.1 Size: 2890×1020 (W×H) 
12.1.2 Distance to front axle: 1600mm
12.1.3 Max. grading depth: 205mm
12.2 Rear ripper
12.2.1 Width: 2087mm
12.2.2 Number of tooth: 5
12.2.3 Max. grading depth: 315mm