## Motor Grader 724MH

Technical Specifications

| No. | Model | Motor Grader 724MH |
| --- | --- | --- |
| 1 | Engine | Model | SC11CB |
|  |  | Rated power | 175kW/240PS |
|  |  | Rated speed | 2300r/min |
|  |  | Max. torque | 750N.m |
|  |  | Max. torque speed | 1500-1700r/min |
| 2 | Operating weight | Front axle | 570kg |
|  |  | Rear axle | 14000kg |
|  |  | Whole machine | 19000/20000kg (standard/with front dozer and rear ripper) |
| 3 | Overall dimension | Length | 9230/10910mm (standard/with front dozer and rear ripper) |
|  |  | Width | 2800/2890mm (standard/with front dozer and rear ripper) |
|  |  | Height | 3550mm |
| 4 | Speed | Gear | 1 | 2 | 3 | 4 | 5 | 6 |
|  |  | Forward (km/h) | 5.74 | 8.73 | 13.02 | 17.49 | 26.98 | 38.98 |
|  |  | Reverse (km/h) | 5.74 | 13.02 | 26.98 | - | - | - |
| 5 | Steering | Frame articulated angle | Left: 25°, right: 25° |
|  |  | Min. turning radius | 8600mm |
| 6 | Max gradeability | 20° |
| 7 | Blade of motor grader | Size | 4422×688mm (length×chord height) |
|  |  | Max. grading depth | 470mm |
|  |  | Max. slant angle | Left: 90°/right: 90° |
|  |  | Rollback angle | 360° |
|  |  | Range of cutting angle | 36°-66° |
| 8 | Dozer | Width | 2890mm |
|  |  | Height | 1020mm |
|  |  | Max. bulldozing depth | 205mm |
| 9 | Ripper | Width | 2087mm |
|  |  | Max. grading depth | 315mm |
|  |  | Number of tooth | 5 |
| 10 | Wheel base of front and rear axle | 6660mm |
| 11 | Wheel tread of motor grader | 2280mm |
| 12 | Max. traction (φ=0.75) | 128.7kN(standard) |
| 13 | Working environment | Altitude | 3500m |
|  |  | Temperature | -28.5-40.4°C |
|  |  | Relative humidity | 78.5% |