## Backhoe Loader 630A

Features of Backhoe Loader 630A:
1. Equipped with WD DETUZ engine
2. 4 forward & 4 reverse synchromesh mechanical shift transmission
3. Combined seal cylinder obtains high seal performance and more reliability
4. Improved loader and backhoe performance
5. CARRARO wet type rear axle with multi-disc brake& CARRARO front axle
6. New-type cab with more space, increases comfort and visibility
7. With 2 wheel driving or 4 wheel driving for option

Specifications of Backhoe Loader 630A:

| Overall Dimension |
| --- |
| 1 | Length(with bucket on ground) | 7085(mm) |
| 2 | Width | 2313(mm) |
| 3 | Load Bucket width | 2313(mm) |
| 4 | Height(To the top of the cab) | 2710 (mm) |
| 5 | Height(To the top of the digging pole) | 3424 (mm) |
| 6 | Wheelbase | 2155.5(mm) |
| 7 | Back wheel Tread | 1700(mm) |
| 8 | Fore wheel Tread | 1880(mm) |
| 9 | Min. ground clearance | 355(mm) for 2WD 275(mm) for 4WD |
| Main Loading Technical Specification |
| 1 | Rated load | 1700(Kg) |
| 2 | Operating weight | 7600KG |
| 3 | Max lifting capability | >2500KG |
| 4 | Rated load bucket capacity | 1.0(m3) |
| 5 | Max. load breakout force | >60kN |
| 6 | Max. dump clearance | 2714(mm) |
| 7 | Max. Dump reach | 845(mm) |
| 8 | Dump angle at any position | ≥43.5° |
| 9 | Min. turning radius |
|  | (1) Outside of bucket | 5280(mm) for 2WD 5670(mm) for 4WD |
|  | (2) Center of front wheel | 3795 (mm) for 2WD 4380(mm) for 4WD |
| 10 | Lifting time of loading bucket | ≤4.5(sec.) |
| 11 | Lowering time of loading bucket | ≤7.5(sec.) |
| 12 | Dumping time | ≤1.5(sec.) |
| 13 | Traveling speed(Km/h),4 forward and 4 reverse |
|  | (1) Ⅰ gear forward | 6 |
|  | (2) Ⅱ gear forward | 9.6 |
|  | (3) Ⅲ gear forward | 20.5 |
|  | (4) Ⅳ gear forward | 38 |
|  | (1) Ⅰ gear reverse | 6.0 |
|  | (2) Ⅱ gear reverse | 9.6 |
|  | (3) Ⅲ gear reverse | 20.5 |
|  | (4) Ⅳ gear reverse | 38 |
| Main Digging Technical Specification |
| 1 | Rated digging bucket capacity | 0.3(m3) |
| 2 | Max. digging depth | 4405(mm) |
| 3 | Max. digging force | >50±10%kN |
| 4 | Max. digging radius | 5481(mm) |
| 5 | Max. dumping height | 3737(mm) |
| Diesel engine |
| 1 | Model | WD DEUTZ WP4G95E221 |
| 2 | Type | Direct injection. Turbocharged. Water cooling |
| 3 | Rated output | 70 (kW) |
| 4 | Total exhaust of cylinder | 4.5(L) |
| 5 | Inter-bore of cylinder/stroke | 102/130(mm) |
| 6 | Voltage of starting motor | 12(V) |
| 7 | Rated speed | 2200(r/min) |
| 8 | Max. Torque | 380(N.M) |
| 9 | Starting type | Electric |
| 10 | Min. specific fuel consumption | 216(g/Kw.h) |
| Transmission System |
| 1. Torque Converter |
| 1 | Model | CARRARO |
| 2 | Cooling type | Pressure oil circulating |
| 2. Transmission case |
| 1 | Model | CARRARO |
| 2 | Type | Synchromesh mechanical shift |
| 3 | Gear shift posit | 4 Forward and 4 reverse gears |
| 3. Axle and Tire |
| 1 | Model | CARRARO |
| 2 | Type of main reducer | spiral bevel gear, single stage |
| 3 | Type of final reducer | Single stage planetary |
| 4 | Max. steering angle | 55° |
| 5 | Tire type | 4WD fore tire12-16.5NHS-10PR |
|  |  | 2WD fore tire11L-16F3-12PR |
|  |  | Rear tire 19.5L-24R4-12PR |
| Working Device Hydraulic System |
| 1 | Model of oil pump | JHP2063C |
| 2 | System pressure | 210(kgf/cm2) |
| 3 | Model of load valve | ZL20.3S4C-00 |
| 4 | Model of excavate valve | WJ20.7SC3-00 |
| Steering System |
| 1 | Type | Fore wheel Steering |
| 2 | Model of steering pump | JHP2063C |
| 3 | Model of Redirector | BZZ5-E160B+ FKB-3022 |
| 4 | System pressure | 140(kgf/cm2) |
| Oil Capacity |
| 1 | Fuel(diesel) | 151(L) |
| 2 | Engine lubricating oil | 11(L) |
| 3 | Oil for converter and gear box | For 2WD | 18.5(L) |
|  |  | For 4WD | 21(L) |
| 4 | Oil for hydraulic system | 110(L) |
| 5 | Oil for driving axles(F/R) | 7.6+17(L) |

we are able to bring many products to the construction machinery and construction equipment market, including: wheel loaders, road rollers, motor graders, skid steer loaders, pavers, concrete truck mixers, Truck Mounted Crane , and we look forward to continuing this service for years to come.