## Truck Mounted Crane (SQ6.3 Straight Boom Crane)

Characteristics
1. As a straight boom crane, the SQ6.3 truck mounted crane uses worm gear reducer to achieve 360°full rotation. 
2. A hydraulic retractable horizontal outrigger whose full span is 5.2m is installed to our lifting machine as standard configuration. 
3. Thanks to its hexagon sections, this material lifting equipment features high lateral stability. 
4. The operating levers distributed near the cargo compartment of the truck mounted crane support both-side operation. 
5. Our truck mounted crane is equipped with 4-function manual main control valves and 4-function manual outrigger control valves. 
6. To guarantee machine operation safety, the hydraulic hoisting machine comes with standard configurations of height limit switch, over winding alarm device and high power LED lights, and optional configuration of moment limiter.

Parameters of Truck Mounted Crane

| Order | Item | Unit | Parameter |
| --- | --- | --- | --- |
| 1 | Maximum load moment | kN·m | 157 |
| 2 | Maximum lifting load | kg | 6300 |
| 3 | Maximum working height | mm | 11500 |
| 4 | Boom length (fully retracted) | mm | 4046 |
| 5 | Maximum lifting height (from the ground) | mm | About 13800 |
| 6 | Lifting ratio |  | 6/4 |
| 7 | Maximum elevation angle of boom | (°) | 77 |
| 8 | Minimum elevation angle of boom | (°) | 0 |
| 9 | Lateral span of the front outrigger | mm | 2130~5210 |
| 10 | Lateral span of the rear outrigger | mm | - |
| 11 | Maximum lifting speed | Main hook (single rope) | Lifting | m/min | 69 |
|  |  |  | Lowering |  | 67 |
| 12 | Rotation speed | r/min | ≤2.5 |
| 13 | Rotation angle | ° | 360° full rotation |
| 14 | Crane weight | kg | 2726 |
| 15 | Fuel pump | ------------- | Gear pump |
| 16 | Fuel tank capacity | L | 140 |
| 17 | Working pressure of hydraulic system | MPa | 23 |
| 18 | Flow of hydraulic system | L/min | 60 |

Rated Lifting Capacity of Truck Mounted Crane (Unit: kg.f)

| R / L | 4.06m | 6.64m | 9.22m | 11.8m |
| --- | --- | --- | --- | --- |
| 2.5 | *6300 | *5000 | 3000 |  |
| 3.0 | *5000 | 3350 | 2750 | 2160 |
| 3.5 | 4000 | 3020 | 2520 | 1990 |
| 4.0 | (3.79) 3800 | 2750 | 2310 | 1830 |
| 4.5 |  | 2500 | 2120 | 1680 |
| 5.0 |  | 2280 | 1950 | 1540 |
| 5.5 |  | 2100 | 1800 | 1410 |
| 6.0 |  | 1950 | 1670 | 1290 |
| 6.5 |  | (6.37) 1800 | 1560 | 1180 |
| 7.0 |  |  | 1470 | 1080 |
| 7.5 |  |  | 1350 | 990 |
| 8.0 |  |  | 1300 | 910 |
| 8.5 |  |  | 1250 | 840 |
| 9.0 |  |  | (8.95) 1200 | 780 |
| 9.5 |  |  |  | 730 |
| 10.0 |  |  |  | 690 |
| 10.5 |  |  |  | 660 |
| 11.0 |  |  |  | 640 |
| 11.5 |  |  |  | 630 |
| Lifting ratio | The lifting ratio is 6 for the items marked with * and is 4 for the other items. |

Welcome to choose Changlin construction machinery (engineering vehicle/construction equipment).