## CLQY100K-I Truck Crane

1. Innovative boom system features built-in slides, flip-sheave boom head, and a telescopic boom with octagonal cross-section. Excellent lifting performance. Maximum safety and reliability. 
2. Patented telescopic boom technology prevents boom breakage or warping of the boom and hydraulic cylinder. 
3. Boom truck has 8 patented technologies built in it, ensuring maximum energy savings, efficiency and smooth lifting, slewing and boom reach adjustment operation. 
4. Torque limiter comes with a color LCD screen for fault diagnosis, delivering industry-leading accuracy. 
5. Large torque hydraulic motor ensures safety during the second lifting cycle. 
6. Ergonomic diver cab provides a large space for easy and effortless operation. 
7. Six proprietary processing technologies ensure the quality of boom truck. 
8. 5-ton counterweight is added to the truck crane.

Technical Specification

| Model | CLQY100K-I |
| --- | --- |
| Length×width×height(mm) | 15600×3000×3850 |
| Operating weight (Kg) | 54900 |
| Diesel engine type | Up VOLVO TAD720VE/ Down Benz OM460LA.E3A |
| Rated output (KW) | 174/360 |
| Max load moment (KN.m) | 3450 |
| Max. total rated lifting capacity (t) | 100 |
| Maximum gradeability (%) | 40 |
| Max. slewing speed (r/min) | 2 |
| Base boom length (m) | 13.5 |
| Max. boom length (m) | 50.9 |