## CLD140-2(S) Bulldozer

Features of CLD140-2(S) Bulldozer 
1. Shang Chai 6135AK-8C type engine has the features of strong power, high torque and excellent reliability. 
2. Optimum design: Novel design and reliable operation allows the machine to offer an excellent visibility in working. 
3. New blade side-tilt function makes earth pushing easier. 
4. Gearbox adopts separate-structured main shaft, making mounting, dismounting and maintenance easier. 
5. Updated power train 
6. A pilot control can be chosen for working equipment of CLD140 to save operating effort.

Technical Data of CLD140-2(S) Bulldozer

| Product model | CLD140-2(S) |
| --- | --- |
| Length×Width×Height(mm) | 5400×4000×3977 |
| Operating weight(Kg) | 15800/17300 |
| Diesel engine type | ShangChai 6135AK-8C |
| Rated output(KW) | 103 |
| Max. lift above ground(mm) | 1020/1000 |
| Max. drop below ground(mm) | 360/350 |
| Track width(mm) | 500/1020 |